# What is MPLS (Multi Protocol Label witching)?

# Introduction

The exponential growth of the Internet over the past several years has placed a tremendous strain on the service provider networks. Not only has there been an increase in the number of users but there has been a multifold increase in connection speeds, backbone traffic and newer applications. Initially ordinary data applications required only store and forward capability in a best effort manner. The newer applications like voice, multimedia traffic and real-time e-commerce applications are pushing toward higher bandwidth and better guarantees, irrespective of the dynamic changes or interruptions in the network.

To honor the service level guarantees, the service providers not only have to provide large data pipes (which are also costlier), but also look for architectures which can provide & guarantee QoS guarantees and optimal performance with minimal increase in the cost of network resources.

MPLS technology enables Service Providers to offer additional services for their customers, scale their current offerings, and exercise more control over their growing networks by using its traffic engineering capabilities. Putting it simply, MPLS is a switching technology used to get packets from one place to another through a series of hops

Multi-Protocol Label Switching (MPLS) provides a mechanism for forwarding packets for any network protocol. It was originally developed in the late 1990s to provide faster packet forwarding for IP routers (see RFC 3031). Since then its capabilities have expanded massively, for example to support service creation (VPNs), traffic engineering, network convergence, and increased resiliency.

MPLS is now the de-facto standard for many carrier and service provider networks and its deployment scenarios continue to grow.

Traditional IP networks are connectionless: when a packet is received, the router determines the next hop using the destination IP address on the packet alongside information from its own forwarding table. The router's forwarding tables contain information on the network topology, obtained via an IP routing protocol, such as OSPF, IS-IS, BGP, RIP or static configuration, which keeps that information synchronized with changes in the network.

MPLS similarly uses IP addresses, either IPv4 or IPv6, to identify end points and intermediate switches and routers. This makes MPLS networks IP-compatible and easily integrated with traditional IP networks. However, unlike traditional IP, MPLS flows are connection-oriented and packets are routed along pre-configured Label Switched Paths (LSPs).

The evident power of the basic MPLS concepts led the industry to define generalized extensions to MPLS, or Generalized MPLS (GMPLS). This work extended the MPLS concept of a label to include implicit values defined by the medium that is being provisioned, for example a timeslot for a SONET/SDH device. So with GMPLS, there is no need for a switch to "read" the label in each packet header. The label is an inherent part of the switch fabric and the switching operations depend on wavelength, or timeslot etc. This permits the benefits of MPLS to be shared by many different types of switching platform.

## MPLS Operation

## How Does MPLS Work?

MPLS works by tagging the traffic, in these example packets, with an identifier (a label) to distinguish the LSPs. When a packet is received, the router uses this label (and sometimes also the link over which it was received) to identify the LSP. It then looks up the LSP in its own forwarding table to determine the best link over which to forward the packet, and the label to use on this next hop.

A different label is used for each hop, and it is chosen by the router or switch performing the forwarding operation. This allows the use of very fast and simple forwarding engines, which are often implemented in hardware.

Ingress routers at the edge of the MPLS network classify each packet potentially using a range of attributes, not just the packet's destination address, to determine which LSP to use. Inside the network, the MPLS routers use only the LSP labels to forward the packet to the egress router.

The diagram above shows a simple example of forwarding IP packets using MPLS, where the forwarding is based only on packet destination IP address. LSR (Label Switched Router) A uses the destination IP address on each packet to select the LSP, which determines the next hop and initial label for each packet (21 and 17). When LSR B receives the packets, it uses these labels to identify the LSPs, from which it determines the next hops (LSRs D and C) and labels (47 and 11). The egress routers (LSRs D and C) strip off the final label and route the packet out of the network.

The above is only one use of MPLS. Since MPLS uses only the label to forward packets, it is protocol-independent, hence the term "Multi-Protocol" in MPLS. It can be used to carry any content (not only packets) over any link technology (using different label encoding for each layer 2 link type).

## IP-based networks typically lack the quality-of-service features available in circuit-based networks, such as Frame Relay and ATM. MPLS bring the sophistication of a connection-oriented protocol to the connectionless IP world. Based on simple improvements in basic IP routing, MPLS brings performance enhancements and service creation capabilities to the network.

MPLS techniques are applicable to ANY network layer protocol, of which IP is the most popular.

Here are some of the terms which are used extensively in MPLS jargon:

1. Forwarding Equivalence Class (FEC): a group of IP packets which are forwarded in the same manner (e.g., over the same path, with the same forwarding treatment).

2. MPLS header: The 32-bit MPLS header contains the following fields:

i. The label field (20-bits) carries the actual value of the MPLS label.

ii. The Class of Service (CoS) field (3-bits) can affect the queuing and discard algorithms applied to the packet as it is transmitted through the network. Since the CoS field has 3 bits, therefore 8 distinct service classes can be maintained.

iii. The Stack (S) field (1-bit) supports a hierarchical label stack. Although MPLS supports a stack, the processing of a labeled packet is always based on the top label, without regard for the possibility that some of other labels may have been above it in the past, or that some number of other labels may be below it at present. An unlabeled packet can be thought of as a packet whose label stack is empty (i.e., whose label stack has depth 0). If a packet's label stack is of depth m, we refer to the label at the bottom of the stack as the level 1 label, to the label above it (if such exists) as the level 2 label, and to the label at the top of the stack as the level m label. The label stack is used for routing packets through LSP Tunnels.

iv. The TTL (time-to-live) field (8-bits) provides conventional IP TTL functionality.

MPLS Header

3. If the Layer 2 technology supports a label field (such as the ATM VPI/VCI or the Frame Relay DLCI fields), the native label field encapsulates the MPLS label. However, if the Layer 2 technology does not support a label field, the MPLS label is encapsulated in a standardized MPLS header that is inserted between the Layer 2 and IP headers.

MPLS, L3 headers

4. MPLS label: is a short fixed length physically contiguous identifier which is used to identify a FEC, usually of local significance.

5. Label Switched Path (LSP): The path through one or more LSRs at one level of the hierarchy which is followed by packets in a particular FEC.

In conventional IP forwarding, a particular router will typically consider two packets to be in the same FEC if there is some address prefix X in that router's routing tables such that X is the "longest match" for each packet's destination address. As the packet traverses the network, each hop in turn re-examines the packet and assigns it to a FEC.

On the other hand, in MPLS, the assignment of a particular packet to a particular FEC is done just once, as the packet enters the network. The FEC to which the packet is assigned is encoded as a label. When a packet is forwarded to its next hop, the label is sent along with it. At subsequent hops, there is no further analysis of the packet's network layer header. Rather, the label is used as an index into a table which specifies the next hop, and a new label. The old label is replaced with the new label, and the packet is forwarded to its next hop.

Fig 2.3 MPLS Operation (from Cisco's site)

## MPLS Benefits

The initial goal of label based switching was to bring the speed of Layer 2 switching to Layer 3. Label based switching methods allow routers to make forwarding decisions based on the contents of a simple label, rather than by performing a complex route lookup based on destination IP address. This initial justification for technologies such as MPLS is no longer perceived as the main benefit, since Layer 3 switches are able to perform route lookups at sufficient speeds to support most interface types.

However, MPLS brings many other benefits to IP-based networks. Forwarding packets based on labels rather than routing them based on headers results in several important advantages:

1. Since a packet is assigned to a FEC when it enters the network, information that cannot be gleaned from the network layer header, can be used for FEC assignment. For example, classification of packets based on the source of the packets.

2. Packets can be assigned a priority label, making Frame Relay and ATM-like quality-of-service guarantees possible. This function relates to the CoS field.

3. The considerations that determine how a packet is assigned to a FEC can become ever more and more complicated, without any impact at all on the routers that merely forward labeled packets.

4. Packet payloads are not examined by the forwarding routers, allowing for different levels of traffic encryption and the transport of multiple protocols.

5. In MPLS, a packet can be forced to follow an explicit route rather than the route chosen by normal dynamic algorithm as the packet travels through the network. This may be done to support traffic engineering, as a matter of policy or to support a given QoS.

In addition to all the above advantages, one of the most important advantages of MPLS is that it is independent of the layer 2 and layer 3 technologies and hence allows integration of networks with different layer 2 and layer 3 protocols.